USE GAME CHANGE PROCEDURE FIRST, IF MACHINE DOES NOT RECOGNIZE GAME IN P10, USE THIS PROCEDURE!!!!!!!!!!

BALLY GAMEMAKER TOTAL CLEAR PROCEDURE

Step 1:

Pull the board

Install Clear Chip in P10

Turn 7 & 8 to ON for DPSW1

Pull any games you want to replace

Install the New Games

Install the board

Power up

Wait for message

Wait for the EPROM & Saferam Erase to complete

Depending on your Mains, you may have to recycle power at this time

Go through Configuration of EPROM & Saferam

Turn Audit Switch to lock in each selection

Power down

Step 2:

Pull the board

Pull Clear Chip in P10

Replace with desired game chip

Set 7 & 8 to OFF for DIP switch SW1

Install the board

Power up

Wait for message

Follow any forced onscreen setup instructions on first powerup

Depending on your Mains, this may or may not include:

Setting up the Currency symbol and Country Options (multi-denomination Main)

Setting up the machine’s Coin Value (or base denomination in multi-denom Mains)

This step could include selecting tokenization, if the Mains support it.

Selecting the denominations that will be available for all games (multi-denom Mains)

Selecting the denominations that each game will use (multi-denom Mains)

Selecting the max (and min) bet options for games that support this.

Double check the following Configuration menu items:

Play Options (to set speed, double up options, if enabled, & game colors.)

Turn On/Off Games (to turn on new games if necessary.)

Hopper/Credit Limits

Cardback Options (if available, to select the card back designs)

Tournament (rare. If tournament chips have been installed and will be used)

You should be up and running.

You might get a message saying new game installed, In that case, try installing the clear chip in P10 once more to enable the game will occupy P10. This may not work with all mains, in which case a complete clear would be required to activate the game that resides in P10.

Set up progressives if desired (see progressive setup documentation)

These are the settings for my machine using 22 Mains:

Jurisdiction – ONE

SAS – 2.83

Chassis Type – UPRIGHT

Coin Acceptor – COIN ACCEPTOR

Bill Acceptor – JCM DBV

Hopper – COIN

Door Type – MECHANICAL

Double Down – ON

Tournament – ON

Primary Host – NONE

Secondary Host – NONE

EFT – DISABLE

Secondary Device – NONE

Typical settings for a V7200 model are as follows:

Jurisdiction – ONE

Primary Host – NONE

Secondary Host – NONE

SAS – NONE

Chassis Type – UPRIGHT

Coin Acceptor – COIN ACCEPTOR and COD BOARD

Bill Acceptor – JCM WBA

Hopper – COIN

Door Type – PULSED OPTIC

Double Down – OFF

Tournament – OFF

EFT – DISABLE

Secondary Device - NON