DETAILED TOTAL CLEAR MACHINE SETTINGS

SafeRAM™ Clear

SafeRAM™ Clear refers to erasing information stored

within battery-backed random access memory (RAM).

A SafeRAM™ Clear is essential before the first use,

when Main program EPROMs are replaced, or if

game memory becomes corrupted.

For a SafeRAM™ Clear, locate DIPSW1 along the

battery side edge of the MPU board assembly and

set DIPSW 7-8 to ON. Some versions of Main programs

require a EPROM labeled “V7S1000CLEAR-02” in

socket P10. Upon ensuring the MPU assembly is

firmly seated into the backplane board, turn the

machine power ON. The message “SAFERAM CLEAR

ENABLED” appears. Actuate the audit key switch.

Follow the displayed instructions by turning power OFF,

setting DIPSW 7-8 OFF, removing the CLEAR-02

EPROM from P10 if installed, and turning power ON.

The screen then displays the settings for CURRENT

JURISDICTION, PRIMARY HOST, SECONDARY HOST, SAS® VERSION,

CHASSIS TYPE, COIN ACCEPTOR, BILL ACCEPTOR, HOPPER TYPE,

DOUBLE DOWN, TOURNAMENT, SECONDARY DEVICE and RESIDUAL

CREDIT MODE.

If the information is correct, the machine can be

restarted by cycling power or pressing the RESET button

located on the MPU assembly.

Set EEPROM Options

If the settings require change, actuate the audit key

switch. Scroll through the available choices with DEAL/

DRAW/START. Confirm each choice with the key switch.

Current Jurisdiction

CURRENT JURISDICTION, or Market Code, designates

specific operation according to the requirements of a

gaming control agency. Some jurisdictions are preset

at the factory. The following table lists current Market

Codes and Jurisdictions.

Jurisdiction 	Market

Locked	VLC

1 	International 60 Hz

2	(Locked) New Jersey

3	(Locked) GLI

4 	International 50 Hz

5 	Default

6 	Uruguay

7 	South Africa

8 	Puerto Rico

9 	Delaware

10 	New Mexico

11 	OLGC

12 	Swiss B No Bet Limit

13 	Swiss A Bet Limit

14 	USAF 2000 Win Limit

15 	USAF No Win Limit

Setup (Cont.)

Primary Host / Secondary Host

A Primary Host and Secondary Host cannot both

use the same protocol. A dual Host system must

use a combination of SAS® (2.xx - 5.xx) and SDS®.

PRIMARY HOST must be set prior to setting SECONDARY

HOST.

SAS® Version

SAS® VERSION refers to the communication protocol

that is compatible with the version of Slot Accounting

System Host computer. The choices for SAS® VERSION

are 2.83, 2.84, 3.11, 3.13, 4.00, 4.02 and 5.01.

Chassis Type

The choices for CHASSIS TYPE are UPRIGHT, BARTOP, or

SLANT. The selection determines the graphical display

of status information when the door is open.

Coin Acceptor

The choices for COIN ACCEPTOR are COIN ACCEPTOR ONLY,

COIN ACCEPTOR AND COD BOARD, or NRI. COIN ACCEPTOR

ONLY and COIN ACCEPTOR AND COD BOARD refer to the

presence or absence of a coin optic decoder (COD)

board (Bally part # AS-03356-0303). Some versions

of Main programs offer choices for Coin Mechanisms,

Inc., CC-62 or CC-16 coin acceptors. The CC-62 does

not require a COD board. The CC-16 does.

NRI refers to the National Rejectors, Inc., brand of

programmable coin acceptors and the processing of

coin information for this acceptor.

Other brands of coin acceptors may be compatible if

they conform to the size and electrical operation of

these acceptors.

Bill Acceptor

The choices for BILL ACCEPTOR are NO BILL ACCEPTOR, JCM

WBA, JCM DBV, GPT, ARDAC, AND MARS 1100 SERIES.

JCM WBA refers to Japan Cash Machine’s World Bill

Acceptor.

JCM DBV selects a communication protocol compatible

with Japan Cash Machine models DBV145, DBV146,

CBA135, SRA135, or IBA135.

GPT selects a protocol for models developed by Global

Payment Technologies.

ARDAC refers to the bill acceptor manufactured by

ARDAC, Inc.

MARS 1100 SERIES refers to the model manufactured

by Mars Electronics International. It is also the correct

setting for the Cashflow™ SC6600.

Printer Type

The Game Maker® will support thermal printers

manufactured by Seiko Instruments, Inc., and

Transact Technologies, Inc. The choices are SEIKO

PRINTER, ITHAKA 800 PRINTER, or NONE. Select one choice

to match the hardware installed in the machine.

Hopper Type

The choices for HOPPER TYPE are COIN, OR NONE. Select

COIN if the machine has a coin-dispensing hopper.

Door Type

The choices for DOOR TYPE are MECHANICAL or PULSED

OPTIC. The selections refer to the sensing device used

to detect the opening of the main door.

Double Down

DOUBLE DOWN is ON or OFF. If ON, the opportunity to

enable and configure this feature will be available

under CONFIGURATION.

Tournament

TOURNAMENT is ON or OFF. If ON, the opportunity to enable

and configure this feature will be available under

CONFIGURATION.

EFT (Electronic Funds Transfer)

The choices for EFT are ENABLE or DISABLE. If enabled,

credits can be added to the machine from a remote

location by the accounting system Host computer.

Secondary Device

The choices for SECONDARY DEVICE are Bally or Anchor.

The choices refer to the manufacturers of the

peripheral device.

Residual Credit Mode

If a machine is configured so that one coin registers

multiple credits (tokenization), it is possible to have

credits remaining after a cashout. The selections for

RESIDUAL CREDIT MODE refer to the disposition of the extra

credits. The choices are NO GAMBLE AND NO ATTEN. PAY,

ATTEN. PAY ONLY, GAMBLE ONLY, and GAMBLE OR ATTEN. PAY.

􀂄The NO GAMBLE AND NO ATTENDANT PAY setting

forces a Player to continue playing until either the

remaining credits equal zero; or they equal the exact

value of a coin from the hopper.

􀂄ATTENDANT PAY ONLY requires an Attendant to

remove the remaining credits from the machine by

turning the Audit key switch and paying the Player.

􀂄GAMBLE ONLY enables a post game where all

residual credits are wagered on a win-lose outcome.

A win results in a coin from the hopper. A loss zeros

the remaining credits. A Player’s chance of winning a

coin is proportional to the residual credits wagered:

If a credit is 1/10th of a hopper coin,

gambling one credit offers a Player

a one-in-ten or 10% chance of

receiving a coin.

However, if nine residual credits are

left, the Player has a 90% chance of

receiving a coin for the residual

credits.

􀂄GAMBLE OR ATTENDANT PAY provides the Player

with all options for resolving residual credits.

Win Evaluation Preference

The choices for WIN EVALUATION PREFERENCE are OHWP/

PLS or LEGACY. If multiple progressive jackpots are

available for the Player, the machine can be

configured to award the largest of multiple eligible

amounts. For example, a straight flush progressive

win will be awarded for a royal flush if the straight

flush progressive amount is larger than the

progressive amount for the royal flush.

To enable the feature, set EVALUATION PREFERENCE to

OHWP/PLS. To establish progressive levels that remain

fixed at the associated win level, set the feature to

LEGACY.

Touch Screen Calibration After

SafeRAM™ Clear

After a successful SafeRAM™ Clear, the Game

Maker® program automatically enters the CAL TOUCH

SCREEN sub menu of the DIAGNOSTICS menu. Follow

the on-screen instructions for hardware and software

calibration.

Currency Format Selection

Following the calibration of the touch screen, the

Game Maker® initialization process requires a

setting for how the bookkeeping records show

monetary information.

One-time configuration after a

SafeRAM™ Clear

Following a SafeRAM™ Clear, on-screen instruction

state that the DIP switches must be reset and special

EPROMs, if installed, removed.

Typical settings for a V7200 model are as follows:

Jurisdiction – ONE

Primary Host – NONE

Secondary Host – NONE

SAS – NONE

Chassis Type – UPRIGHT

Coin Acceptor – COIN ACCEPTOR and COD BOARD

Bill Acceptor – JCM WBA

Hopper – COIN

Door Type – PULSED OPTIC

Double Down – OFF

Tournament – OFF

EFT – DISABLE

Secondary Device – NONE

Note: If machine comes up in demo mode, which will happen if the version of the Mains installed requires you to set an SAS protocol, you must give it a terminal id under Host Configuration. This is the first selection of the Configuration menu in the far-right colum on the setup screen. Just keep entering 1's (9 times) until the red save square lights up and save the setting. The machine will exit demo mode and will turn on the dbv and coin mech. The bookkeeping meters will also be activated.